## Slide 1: Surviving Inspection MRA Education Day October 27, 2018
Presented by
Kevin Genson
kgenson@firstchesapeake.org
Senior Robot Inspector Chesapeake District

## Slide 2: Agenda
Purpose and Goals
Event Flow
Inspection
Final Thoughts

## Slide 3: Priorities and Goals
Robot Inspectors are your friends
Three Priorities
  Safety
  Compliance
  Fun
Goals
  Get all teams on the field for ALL matches
    Teams must pass inspection to compete
    Not being on the field hurts your own team and alliance partners
  Help teams improve their robots

## Slide 4: Pre-Inspections
FIRST allows lead robot inspectors (LRIs) to conduct pre-inspections.
  Opportunity for teams to discover potential problems and solve them during unbag time.
  Do not impact inspections during events.
FIRST Chesapeake will be doing pre-inspection events again on February 23, 2019.
  Manassas
  Richmond
  Newport News
  Maryland (Location TBD)
Additional pre-inspections may occur if depending on team needs (e-mail me).

## Slide 5: Pre-Inspections
LRIs will be available during established times at each location.
Students are not required for pre-inspections.
Process:
  Inspector greets you.
  Robot is unbagged.
  Inspector evaluates robot and provides recommendations.
  Robot is bagged.
Do not unbag the robot unless authorized.
No work will be permitted on the robot during inspection.

## Slide 6: District Event Flow
Day 1 (6:00PM-10:00PM)
  Pits Open: load-in and teams set-up pits
  Bag & Tag Compliance checks and unbagging of robots
  Inspection can begin immediately!
Day 2 (Qualification matches start at 11:00AM)
  Finish any last inspections (goal is to have none!)
  “Random” inspections throughout the day
  Re-inspections when asked
Day 3
  “Random” inspections and re-inspections
  Re-inspection for playoff robots

## Slide 7: Championship Event Flow
Wednesday (5:00PM-9:00PM)
  Pits Open and teams set-up pits
  Bag & Tag Compliance checks and unbagging of robots
  Inspection can begin immediately!
Thursday
  Finish any last inspections (goal is to have none!)
  Practice matches (10:00AM-12:30PM)
  Qualification Matches start at 2:00PM
Friday & Saturday
  “Random” inspections throughout the day
  Re-inspections when asked
  Weigh-in for playoff robots (Saturday)

## Slide 8: Key Points
Start Inspection Early
  Locate major problems early
  Easier to get improvements/changes re-inspected
  Once passed, can utilize standby practice line
Inspectors
  Help and guide teams through the inspection process
  Want to speak primarily to students
Getting Started
  Send a representative to the inspection station and ask to be inspected.
  Do not just bring your robot to be weighed

## Slide 9: Bag-Tag Forms
Take a picture of your lock-up form every time you bag the robot.
Inspectors are not required to physically hold or sign the form, only verify that your team followed procedures and that everything is properly documented.

## Slide 10: Initial Inspection

## Slide 11: Unbagging
DO NOT UNBAG YOUR ROBOT UNTIL AUTHORIZED
  You will be forced to stop and will likely have to wait several hours
Make sure your bag-and-tag form is signed and ready as soon as you enter the pit
  Inspectors will be eager to sign you out
  Designate a team member as being responsible for the form
  Take a picture of the form before you leave
  Do not put the form inside the bag
If you are found to be noncompliant, the LRI will have to get several signatures and this takes time.
Repeat offenders will require that I notify FIRST HQ and establish penalties.
  This can be up to losing an entire day of unbag time.

## Slide 12: Initial Inspection
Weight
  Robot
    Remove battery and bumpers
    Include all robot mechanisms
  Bumpers
    Weigh each set individually
    Include all mounting hardware
  Team places items on scale
  DO NOT STEP ON SCALE
Size
  Remove bumpers
  Inspection method varies over years

## Slide 13: Initial Inspection
Continue in Pit
  Minimize representatives in pit
    Prefer 2 key students
  Ensure all stored energy in lowest energy state
    Turn off robot
    Relieve pressures (i.e., air in storage tanks)
    Release springs / surgical tubing / bungee cords, etc.
  Team must prove robot is safe

## Slide 14: Bumpers
Bumpers (Red & Blue)
  Construction
    Proper plywood backing
    Pool noodles
    Durable fabric cover
    Proper display of team number
  Mounting
    Securely fastened
    Ease of removal
  Pay particular attention to gaps
    No gaps in corners
    Minimum corner coverage

## Slide 15: Bumpers
Bumpers are not an afterthought!
  They are a mandatory part of the robot
  Bumpers can easily disqualify a robot if not robustly constructed
Design and build early in the build period
  Robust design that can withstand impact
  Easy and intuitive mounting system
  Double-check corners for no gaps
Avoid bumper covers or convertible bumpers

## Slide 16: Mechanical Inspection

## Slide 17: Mechanical Inspection
Bill of Materials (BOM)
  Please have one ready
  Total cost of materials <= limit
  Total cost of any one component <= limit
    KOP components excluded
    Typically a lower limit for excludable components
  Cost = Material + Labor
    Labor from team members and recognized team sponsors are excluded
  Can be provided in printed or electronic form
  Put a copy on Google Drive or take a picture

## Slide 18: Mechanical Inspection
Sharp Edges and Protrusions
  Hazard to personnel or field
    Leading edges of the robot (surface area of at least 1 in2)
    Edges (minimum radius of 0.030)
    Points and corners (minimum radius of 1/8-inch)
    Undersides
  Improperly cut tie-wraps
  Areas of concern
    Robot parts that interact with game pieces
    Near 120 amp breaker
    Near battery connections

## Slide 19: Mechanical Inspection
Safe Energy Storage
  One approved battery
    2018 rules allowed certain USB power packs.
  Springs, surgical tubing, bungee cords, etc.
  Pressurized air in storage tanks
  Stored mechanical energy must be safe to be around
    Consider who will be working around the devices
    Teams must prove that their designs are safe
Securing Batteries
  Battery must be secure (turn the robot upside down and shake it)
  2” cinch strap (left) works well
  Recommend avoiding the use of electrical energy storage that could stay charged after the robot is shut down (supercaps)
Battery Tray for AM14U Series (am-2939)
2” Cinch Strap (Amazon)

## Slide 20: Mechanical Inspection
Pneumatic Storage
  Storage tanks must be rigidly secured
    Please avoid cable ties or tape
    Cable ties are legal but rarely secure tanks well and can stretch over time
    Tape is illegal on pneumatic components
    Avoid using banding that could cut into the storage device
  Preferred method are clamps or brackets
  Consider using something other than a Clippard tank if you require a lot of air
Bracket for Plastic Air Tank
(am-2008)
0.89 Gallon Aluminum Tank
(Lowriderdepot.com)

## Slide 21: Mechanical Recommendations
Clip your cable ties as short as you can get them
Run your hands over every part of the robot and file down accordingly
Ensure your battery is secure but easy to remove
  Constrained in every direction
  Minimal movement
Properly secure pneumatic storage
  COTS solutions are preferred
  Clamping is better than cable ties
  If the storage tank can move it will undergo scrutiny

## Slide 22: Mechanical Recommendations
If ballast is used, it must be in compliance with the rules
  No additional batteries
  Must not pose a threat to personnel, field, or other robots
    No exposed lead (uncoated dive weights)
    Avoid containers of loose fasteners or ballast
Ballast must be secured to the robot
  Containers of loose material will undergo particular scrutiny

## Slide 23: Electrical Inspection

## Slide 24: Electrical Inspection
Breaker visibility is extremely important
  Robots have escaped the field
  Imagine you’re a stranger with seconds to disable a robot
    Can you find the breaker?
    Can you disable it?
Design for access and provide plenty of signage
  Labeling not required but highly recommended
  Ask a total stranger to turn off your robot and see what they do
Consider potential for other robots and game pieces to disable breakers

## Slide 25: Electrical Inspection
Robot Radio
  Make it a priority to get the radio programmed immediately
  Mount the radio high and away from metal
    Avoid clamping the radio (cable ties)
    Use adhesive hook-and-loop tape
  Radios power has been a source of issues
    Secure connections with tape or adhesive
    Consider Power Over Ethernet (POE)
    Can use both POE and plug
Power Distribution Panel
  Must be visible for inspection
  Accessibility is key for good design

## Slide 26: Electrical Inspection
https://www.chiefdelphi.com/forums/showpost.php?p=1694886&postcount=286

## Slide 27: Electrical Inspection
A CUSTOM CIRCUIT is any electrical COMPONENT of the ROBOT other than motors, pneumatic solenoids, roboRIO, PDP, PCM, VRM, RSL, 120A breaker, motor controllers, relay modules, wireless bridge, or batteries.
  Any active electrical item that is not an actuator or core Control System item
  CUSTOM CIRCUITS shall not produce voltages exceeding 24V
  Can’t directly alter power pathways
  High impedance voltage monitoring or low impedance current monitoring acceptable
  Can’t directly control motor controllers or relays
Can be connected to the CAN bus
  CUSTOM CIRCUITS shall not interfere with, alter, or block communications among the roboRIO, PDP, PCM, and motor controllers
All remote cameras that broadcast a signal (e.g., use WiFi) used have to be pre-approved by FIRST

## Slide 28: Electrical Recommendations
The best thing you can do is have clean, well-labeled wiring
  Easy inspections
  Easy troubleshooting
Use quality connectors such as Anderson Powerpole
Consider using larger gauge wire
  10 gauge for motors
    “Easy-ID Low Voltage Cable”
  4 gauge for battery
    “Ultra-Flexible Battery Wire”
Pull on every connection and verify nothing is loose
Consider using perforated sheets for electrical mounting
  “High-Strength PVC Plastic Perforated Sheets”
Consider investing in a hydraulic crimper

## Slide 29: Electrical Recommendations
Avoid making assumptions when it comes to motors, solenoids, or custom circuits
  Use the FRC Q&A System
  Feel free to contact me ahead of time for additional clarification
  Pre-inspections are great for this
A good example is “automotive motors”
  Will require evidence that the motor is actually for automotive use
Avoid using any kind of clamping action to secure your radio
  This can cause the radio to have intermittent connectivity due to how the antenna is located inside the casing.
  One solution that seems to work well is to use sticky-backed hook/loop tape such as 3M Dual Lock.
Examine the location of your circuit breaker and think about what is the potential risk of a field element (or another robot) accidentally turning your robot off.

## Slide 30: Pneumatics Inspection
Pneumatics

## Slide 31: Pneumatics Inspection
Minimum Components
  Pressure gauge to show the “stored” air pressure (<= 120 psi)
  Pressure gauge to show the “working” air pressure (<= 60 psi)
  A Pressure Relief Valve calibrated to release at 125 psi as close to compressor as possible
    Prefer a rigid connection to compressor
  A Pressure Switch connected to the Pneumatics Control Module and calibrated (<= 120 psi)
  A Vent Plug Valve that vents the stored air to atmosphere
    Should be easily accessible
    Must vent “high side” of system to atmosphere
  Pressure Relieving Regulator to relieve back-pressure from devices and maintain a 60 psi “working” pressure

## Slide 32: Pneumatics Inspection
No modifications to components except:
  Remove mounting pin from cylinder
  Wiring modified to connect to control system
  Do not paint or tape over components
Compressor
  Any type allowed if meet specs
    Teams need to show documentation
    KOP compressor is actually undersized
      0.88 cfm vs 1.10 cfm limit
  Only one can be used
    Can be off-board
      Must still be controlled by robot
      Minimal pneumatics must still be on robot

## Slide 33: Pneumatics Inspection
Pneumatic Solenoid Valves
  Non-KOP Solenoid valves are restricted to 1/8” NPT port diameters
    Teams need to provide documentation
  If solenoid valves rated below 125 psi are used, an additional pressure relief valve must be added to the “working” pressure circuit and set to a lower pressure than the valve rating
  Only one solenoid per pneumatic actuator
  Controlled by Spike relay or NI 9472 Digital Output module

## Slide 34: Pneumatics Recommendation
Perform your own pneumatics check
  Check the high pressure gauge shows <= 120 psi
  Check the working pressure gauge shows <=60 psi
  Compressor should stop at 120 psi or less
  Check operation of pneumatics relief valve
    Short the leads of the switch
    Make sure relief valve relieves at no more than 125 psi
  Static pressure relief valve (right) superior option
Treat pneumatics like an electrical system
  Cleanly lay out and label your tubing
  The easier it is to inspect, the easier it is to troubleshoot
  Simplify as much as possible (the tank on the right is equivalent to 6 Clippard tanks)
Ensure your gauges, regulators, dump valve, relief valve, and switch are easily accessible
The AndyMark 1.1CFM compressor can get hot enough to melt tubing.
Pressure Relief Valve
(McMaster-Carr 48435K714)

## Slide 35: Pneumatics Inspection
Not Allowed !!
White Clippard P/N: AVT-PP-41
Threaded End

## Slide 36: Follow-On Inspections
Have inspectors re-certify all changes to the Robot, with the exception of:
  Adding/removing fasteners or labeling
  Changes to code
  Replacement of components and mechanisms with identical units
  Additions, removals, or reconfigurations of robot with previously inspected subsets of mechanisms
When in doubt, ask.

## Slide 37: Disputes
Unfortunately there will be disagreements.
If you disagree with the ruling of an inspector, please contact the LRI (or the RI may do so)
  RIs are responsible for inspecting robots
  LRIs are responsible for customer service
If you disagree with the LRI, you have the right to escalate the dispute to the SRI (me)
  The LRI will contact me directly
If you disagree with me, you have the right to request that I contact Al Skierkiewicz, FRC Chief Robot Inspector
  I will coordinate with Al and get a final ruling
  This is not likely to be a fast process
If you disagree with Al, too bad.

## Slide 38: Design Recommendations
Do not assume the field is perfectly engineered
  Broken ropes in 2016
  Field elements getting damaged or bent during play
  It may be the field’s fault, but it’s still your problem
A simple robot that works perfectly is better than a complicated robot that can’t be trusted
Design your robot as if everyone is out to destroy you
  Emphasize ruggedness and survivability
  Design for reliability and repair

## Slide 39: Questions?
kgenson@firstchesapeake.org