## Slide 1: Chassis / Drive Train 101
Tom Milnes
Team 2199 Systems Mentor
Principal Mathematician JHU/APL
Notes: Introduction by Mr. Milnes

## Slide 2: Chassis / Drive Train
Chassis / Drive Train are foundational elements of your robot
  Without the chassis you have no where to place manipulators / drive system and electrical components
  Without drive train the robot doesn’t move
    Impossible to score any points
    Often it is possible to score points by moving past a line in autonomous

## Slide 3: What is a Chassis / Drive Train?
Chassis (Merriam Webster Online)
  The supporting frame of a structure (as an automobile, television, or robot)
Drive Train (Mr. Milnes’ Definition)
  The assembled parts including motors, gearboxes, gears, chains, belts, wheels that make a vehicle move

## Slide 4: Chassis
The Foundation for Everything!

## Slide 5: Chassis Shape
Rectangular is the #1 choice of FIRST teams
  Simple to construct yet gives plenty of options
  Biggest decision is
    Narrow Robot – Wheels placed on longest sides
    Wide Robot – Wheels placed on shortest sides
Direction of Travel
Direction of Travel
Notes: Matt

## Slide 6: Narrow or Wide?
Depends on the Game Being Played
  Want chassis that will allow you to score the greatest number of points / game
  Need to figure out your game strategy / manipulators to implement first
Example 2014 Game
  Had a 24” diameter ball which you probably wanted to get on your robot so you could transport it and score it in a goal
  Had a perimeter limit of 112”

## Slide 7: Narrow or Wide?
24”
25”
1”
27”
2 x 27” + 2 x w <= 112” Max Perimeter
w <= 29”
Notes: Abi

## Slide 8: Narrow, Wide, Square?
Everything being equal here are Pros / Cons for Narrow / Wide
Narrow
  Harder to block going forward but harder to block other robots
  Can segment robot into manipulator section (FWD) and electronics / pneumatics section (AFT)
  Less precise turning but quicker
  Will pick up fewer objects at a time (objects back to back)
Wide
  More precise turning but slower
  Manipulator section in center of robot electronics / pneumatics on side
  Easier to block other robots and vice versa
  Will pick up more objects at a time (objects side to side)
Square
  Game element is large and with comparable length and width
Notes: Abi

## Slide 9: Chassis Material
Must be strong enough to hold everything else in place
Must be light enough so you can add drive train and manipulators and stay within weight limit (120 pounds)
Options
  Steel – Strong but Too Heavy!
  Wood – Light but Too Fragile!
  Aluminum – Just Right!!
  Exotica – Graphite, Fiberglass, …
    Not a good idea for an inexperienced team!
    Not a good idea if you haven’t mastered the technology in the offseason (including reliability testing)
    Must be able to be repaired!
Notes: Matt

## Slide 10: Chassis – Custom or COTS?
Custom
  Machined from CAD drawing
  Constructed by hand from square or rectangular tubing
COTS – Commercial Off The Shelf
  Robot Parts or Manufacturing Retailers
    80-20 - https://8020.net/ “Industrial Erector Set”
    AndyMark - http://www.andymark.com
    Vexpro - https://www.vexrobotics.com/vexpro

## Slide 11: Custom-CAD?
Machined from CAD drawing – ONLY IF
  You have several CAD experts
  You have a dedicated machine shop that works quickly
  You have successfully done this in previous years or in the offseason

## Slide 12: Custom-By Hand?
Constructed from square, rectangular and C channel aluminum tubing which is hand drilled
  Quickly available at Home Depot except C-Channel
  Not recommended – slow to build and imprecise
Square and Rectangular
C Channel

## Slide 13: COTS Chassis Parts
Dedicated Robotics or Engineering supplier
Recommended for rookie, inexperienced, small or under-resourced teams
Lots of good options from
  80-20, AndyMark, Vexpro

## Slide 14: 80-20 Chassis Parts
1010 Profile 80-20
1”x1” profile
.51 pounds / ft
Generally utilizes ¼”-20 bolts for fastening but has #10-32 options
80-20 Robot Chassis

## Slide 15: 80-20 Fastening
100’s of fastening
Options with 80/20
T-Nut

## Slide 16: 80-20 Parts
L-Bracket
Roller Set
(Linear Motion)
Pivoting
Assembly
80-20 has parts for chassis and manipulator construction including
And 1000’s more!

## Slide 17: AndyMark Chassis Parts – Rev Robotics* Extrusion
4’ Rev Robotics
1” Extrusion
1”x1” profile
.44 pounds / inch
Uses #10-32 bolts with jam nuts
(#10 = .2”)
*Founded by Greg Needel – FIRST Chesapeake Alumni
http://www.revrobotics.com

## Slide 18: AndyMark Chassis Parts – Rev Robotics* Extrusion
L-Bracket
Linear Motion
Pillow Block
Rev has parts for chassis and manipulator construction including
And 10’s more, but several which are made specifically for FRC

## Slide 19: AndyMark Chassis Parts – C-Channel
30” C-Channel
am-2222
.41 pounds / ft
¼” holes every 1”, 1/8” thick
1.25” x 1.125” exterior profile
1” x 1” interior profiles – plays well with 80-20 or Rev 1” Extrusion
Also
72” C-Channel
am-3052
.43 pounds / ft

## Slide 20: AndyMark Chassis Parts – Nano Tubes
Combines chassis, gearbox (single speed only), and chain/gears/belts
  However interior free versions are available
Comprise the inner two rails in a rectangular drive system
Come in 20” and 31” sizes, with two motor inputs
Linear density of about .9 pounds / foot for chassis components

## Slide 21: AndyMark Chassis Parts – Nano Tubes
20 Inch Nano Tube
Chained Drive
31 Inch Nano Tube
Gear Drive
31 Inch Nano Tube
Chassis Only

## Slide 22: AndyMark Chassis Parts – Nano Tube Robot*
*Outer Chassis Required

## Slide 23: AndyMark Kit Chassis Options
AndyMark C-Base
AndyMark AM14U
Both Kits have holes that cause the center wheels
in 6 wheel tank drives to be lower than forward and rear wheels
9 pounds
11.3 pounds
for max size

## Slide 24: VexPro VersaChassis
No kit available but all the parts!
Plays well with VexPro equipment
Requires lots of drilling
For Wheels and
Gearboxes
2”x1” VersaFrame Stock
.66 pound / ft
.1”thick walls
Uses #8-32 (.177”) bolts and nuts
Lighter duty compared
To 80-20 or AndyMark

## Slide 25: Chassis Pan
Placing a rectangular sheet on the bottom of the chassis adds to rigidity of frame and is a good mounting location for battery, electrical components, Robo-Rio, Compressor, Air Tanks, …

## Slide 26: Chassis Pan Options
AndyMark PVC Pegboard
White Pegboard
¼” holes every inch
Approximately $3.5 / sq. ft.
¼” holes every inch
$1 / sq. ft. at Home Depot
Both are electrical insulators

## Slide 27: Open Chassis
X
If the game requires you to pick up game pieces off the floor an open chassis is a good option.
You’ll probably need some way to reinforce the open end of the robot so both sides don’t wiggle
Stuff that would have gone in chassis pan need to be placed elsewhere, ideally light weight stuff

## Slide 28: Open Chassis
Stuff that would have gone in chassis pan need to be placed elsewhere, ideally light weight stuff
  Vertical mounting planes preferable to horizontal

## Slide 29: Center of Mass
Robot naturally translates and rotates about its center of mass
  The 3-D balance point
Stability and Mobility increases when CM is low and centered
  Put light parts high as needed
  Keep heavy parts low
Battery motors pump, etc.
Battery motors pump, etc.
Ms. Mobile
Mr. Tippy

## Slide 30: Center of Mass
Ideally for a closed chassis robot battery would be in the center of the robot on the chassis pan
If not possible (many open chassis designs) compensate by moving other heavy objects to counterbalance battery
  For instance drive gearboxes and motors
  Always keep battery low!!

## Slide 31: Chassis Summary
Choose Narrow or Wide Chassis based on your chosen game strategy / chosen manipulators
Construct chassis out of aluminum parts
Choose COTS or Custom (CAD / Machine Shop) based on your team’s experience level
  Avoid trying something you haven’t already done in previous years or in the offseason
Place pan at bottom of chassis for mounting stuff if closed chassis
Consider open chassis when game pieces are on floor
  Place electronics / pneumatics on vertical planes
Keep center of mass low and centered

## Slide 32: Drive Train
Let’s Make That Robot Move!

## Slide 33: Drive Train – Components
Motors
  Converts electrical power to mechanical power at low torque and high speed
Gearbox
  Converts mechanical power to higher torque and lower speed
Chain, Belt, or Gears
  Transmits mechanical power to wheels
Wheels, Tracks
  Rotate to move the robot

## Slide 34: Drive System - Motors
CIM
  #1 Choice – Rugged and made for continuous usage
Other alternatives
  RS 775 or 550 with CIM-ile adaptor or Mini-CIM
    Used when some CIMs are needed for heavy duty manipulators
    Used to increase robot traction if not needed for manipulators
CIM Motor
CIMile
RS 550
Mini CIM

## Slide 35: Drive System - Gearboxes
COTS
  AndyMark and VexPro
  Single Speed or Dual Speed (shifting)
  2 or 3 motor versions
Custom
  Only if you have already built one in the off-season
  Can have parts custom machined quickly
  Not recommended for small, rookie, or inexperienced teams!!

## Slide 36: Single Speed vs. Shifting
Single Speed Gear Boxes are simpler
  But you have to choose a single speed / torque range
    Fast speed and low torque – offensive robot
    Medium speed / medium torque – compromise robot
    Low speed / high torque – defensive robot
Shifting is more complicated because of the need for pneumatic or electrical actuators
  But can shift from high speed / low torque to low speed / high torque
  Can play offense and defense equally well

## Slide 37: AndyMark Single Speed Gearboxes
LJ Bevel Box
CIMple Box
Toughbox Mini
Nano Tube 31
Nano Tube 20
EVO Slim 2
$59
$129
$89
$281
$286
$110

## Slide 38: AndyMark
Lots of Choices
AndyMark gearboxes generally use US Digital Encoders
  US Digital encoders can be finicky!!

## Slide 39: US Digital Encoder
Some people swear by them!
Some people swear about them!
$42

## Slide 40: VexPro Single Speed Gearboxes
Single Speed Single Reduction
Single Speed Double Reduction
Single Speed West Coast Drive
$60
2 CIM Only
$65
$90

## Slide 41: VexPro SS Gearboxes
Not as heavy duty as the Toughbox
  Support long shafts!!
  But very affordable!!
Use Greyhill 63R Mechanical Encoder
  Very reliable and easy to use
$56

## Slide 42: VexPro Single Reduction Clamping Gearbox

## Slide 43: VexPro Single Reduction Clamping Gearbox
Have to use 1” x 2” Versaframe tube or equivalent.
If so, may be a good choice in a single speed gearbox since it is very light

## Slide 44: AndyMark Shifting Gearboxes
EVO Shifter
2 or 3 CIM Variants
Machined to AM14U
Bolt Pattern
Multiple Gear Ratios
Sells for $325
Super Sonic Shifter
2 or 3 CIM
Simple Rectangular
Bolt pattern
Fixed High / Low
Ratios
Sells for $319
Sonic Shifter
2 CIM only
Multiple Gear Ratios
Sells for $279
Extremely Rugged Designs

## Slide 45: AndyMark Shifting Gearboxes
Very Heavy Duty
  Typically don’t need shaft support
Use US Digital Encoders
  Light Duty
Servo and Pneumatic Shifting
  Servo will not support shifting on the fly

## Slide 46: VexPro Shifting Gearboxes
3 CIM Ball Shifter
West Coast Products
Dog Shifter
$110
$240
More Affordable than AndyMark two speed shifters, but lighter duty

## Slide 47: VexPro Shifting Gearboxes
Not as heavy duty as AndyMark
  Very attractively priced
  Will have to support long shafts!
Pneumatic Shifting Only
  Guaranteed shift on the fly
Uses Mechanical Greyhill 63R Encoder
  Very reliable and easy to use

## Slide 48: Power Transmission
Belts
  Efficient and grease free
  Can’t change length
  Use either canned design (AM14U) or be very precise in designing (flexible wheel location)
  Requires pulleys that match belts used
Chains
  Can “break chain” to change length
  Difficult to get perfect length even using half links ->
    Chain Tensioner
    Axle Position Adjuster
      FRC Specific
      Pillow Blocks

## Slide 49: Chain Tensioners
Adjustable Arm
Chain Tensioner
Floating Chain
Tensioner
Ring or Sprocket
Tensioner
Available at McMaster Carr https://www.mcmaster.com
The “Industrial Wal-Mart”

## Slide 50: Axle Position Adjusters for FRC
VexPro Drive Bearing Block
221 Robotics RockBox Chassis
Cam Bolt

## Slide 51: Pillow Blocks
Examples from McMaster Carr
Need to use 80-20 or Rev Extrusion to allow adjustment of axle location to tighten chain
Low Profile
Mounted
Vibration Damped

## Slide 52: Power Transmission
Gears
  Very rugged but requires extreme precision if hand made
  COTS solutions such as Nano Tube from AndyMark or VexPro Clamp On are attractive alternatives to hand made
  Can be heavy if a lot of gears are used

## Slide 53: Power Transmission
Direct Drive
  Used for centered wheel in West Coast Drive
  Used for Omni, Mecanum, and Swerve Drive systems
  Most reliable but may require more gearboxes if used for all wheels
  Mounting gearbox to frame to achieve direct drive can often be challenging
    Consider mounting and axle support methods before buying a gearbox
VexPro Direct
Drive Example

## Slide 54: Wheels, Tracks

## Slide 55: Solid Rubber Wheels
Intermediate traction but allows some sideways skid for turning
Smaller rubber wheels are easier to turn (4”)
AndyMark
Colson

## Slide 56: Traction Wheels
  Highest traction but resistance to side skidding can complicate turning
    May choose traction wheels as center wheels and something else for front and back
AndyMark
VexPro

## Slide 57: Pneumatic Wheels
Intermediate Traction
Excellent for overcoming bumps or obstacles
Resistance to skidding can make turning somewhat difficult – may require extreme center wheel drop
AndyMark

## Slide 58: Omni Wheels
Small rubber wheels mounted sideways
  Intermediate traction forward but moves sideways freely so turning not a problem
AndyMark
VexPro

## Slide 59: Mecanum Wheels
Skateboard wheels rotated 45 to main wheel frame
  Requires an entire set to implement “Mecanum Drive” with rollers making a “X”
AndyMark
VexPro

## Slide 60: Mecanum Drive

## Slide 61: Mecanum Drive
If front wheels move in opposite direction to back wheels vehicle moves sideways
  Called strafing
Gives two directions of freedom in translation
  Robot is extremely nimble!
Mecanum wheels are expensive!
Traction is compromised due to rolling elements and 45 angle
For the right game can be an excellent choice

## Slide 62: Tank Treads
AndyMark Rhino Tank Drive

## Slide 63: Tank Treads
Not a nimble turner but fast going straight
Good choice for obstacle defeat
Probably best to get a Tread System
  Tread and Roller Wheels
Expensive!!
  AndyMark product $369 per side

## Slide 64: Drive Type
Lamborghini

## Slide 65: Arcade Drive
All cars use Arcade Drive
  Front Wheels Turn, Rear Wheels fixed

## Slide 66: Arcade Drive
Big Problem
  Makes really large turns!!
  FRC Fields can require tight turns!
2017 Field

## Slide 67: Tank Drive
M1A1 Abrams Tank

## Slide 68: Tank Drive
For FIRST Robotics “Tank Drive” means wheels on left and right sides are driven independently – normally with two joysticks
  Only a single gearbox per side
  Can turn in place, go forward and backward
  Good combination of simplicity and performance
    The most popular drive system in FIRST!!

## Slide 69: Tank Drive
Gearboxes
Wheels
Chain or Belt
Motors

## Slide 70: Tank Drive
How does a wheeled tank
drive robot turn in place
with the narrow wheels
pointed in a single direction?

## Slide 71: Some Tank Drive Turning Solutions
#1 Lower the center wheels slightly
Use omni wheels at the end of the robot
  Causes loss of traction
  Can be turned easily by other
  robots!
C-Channel
Axle Locations
Omni

## Slide 72: Not So Good Tank Drive Turning Solutions
Using caster wheels (which turn in any direction) is a tempting solution.
PROBLEM
  Undriven caster wheel reduces weight on driving wheels
  Reduced traction on Driving Wheels
SOLUTION
  All wheels need to be powered!!
Caster Wheel

## Slide 73: Holonomic (2-D Translation) Drive Systems

## Slide 74: Mecanum Drive
Complete Mecanum Chassis / Drive Train
From AndyMark

## Slide 75: 4-Omni Drive
Uses 4 Omni Wheels configured in a “+” or “x” configuration

## Slide 76: 4-Omni Drive
Highly maneuverable but has less traction than even the mecanum drive
  Only ½ of the motors are pushing in any direction
  Not recommended

## Slide 77: H-Omni Drive

## Slide 78: H-Omni Drive
Basically a Tank Drive with a Slider Wheel
More traction than 4-Omni Drive but lots less than tank drive
Requires only 3 gearboxes
Not a bad choice for 2015 game Recycle Rush
  Since opposing alliances were on opposite of field with no defense played

## Slide 79: Exotica

## Slide 80: Swerve Drive
4 wheels with separate gearboxes that can rotate in any direction

## Slide 81: Swerve Drive
Point the wheels in the direction you want to translate

## Slide 82: Swerve Drive
Rotate wheels in a circular pattern to rotate robot

## Slide 83: Swerve Drive
AndyMark Swerve
Drive System
$325

## Slide 84: Swerve Drive
Highly Capable
  2-D translation and rotation without loss in traction
Is a complete transmission system
Extremely expensive
  A single swerve drive assembly (1 wheel apiece) costs $325 or more
    Requires 1 CIM drive motor and 1 other motor to rotate wheel
Very complicated to program
Not recommended for rookie or inexperienced teams
Should be mastered in off-season

## Slide 85: Transforming Drives
Butterfly Drive
Either
4 traction wheels for pushing
4 omni wheels for maneuverability
Octanum Drive
Either
4 traction wheels for pushing, straight running
4 mecanum wheels for maneuverability

## Slide 86: Pneumatic Drive System Change
Traction
Wheel
Mecanum
Wheel
Pneumatic
Piston
Drive Axle
Sprocket /
Pulley
Chain / Belt

## Slide 87: Drive Systems
Lots of choices!
Choose drive system and drive system components based on
  Required robot performance according to game strategy
  Experience with components and systems
  Financial and Weight budgets