## Slide 1: Motors 101
Tom Milnes
BAA Team 2199 Representative
Principal Mathematician JHU/APL
Notes: Introduction by Mr. Milnes

## Slide 2: Why Use Electrical Motors?
High Torque or Speed Rotational Motion Is Needed
  Low Torque, Speed, with finite rotation can achieved with Servos
Variable speed / force linear motion is needed over long distances (using cord or chain)
  Two position linear motion better achieved with pneumatics over achievable ranges
  Motion prevention is also better done with pneumatics
    Pneumatic device pins a manipulator part into place
Notes: Matt

## Slide 3: What is an Electrical Motor?
Device which converts Electrical Power to Mechanical Rotational Power
Notes: Matt

## Slide 4: What is Power?
Power is the rate of Energy production
  Power = Energy / Time
Notes: Matt

## Slide 5: What is Energy?
Physics Inspired English Definition
  Energy is required to do Work
Energy Sources
  Battery, Stretched Spring, Gasoline, Moving Object, Object at Height
  Can be converted from / to various forms
    Total is conserved
    But some is usually converted to useless forms such as heat
Notes: Abi gives as Drive System / Chassis lead

## Slide 6: What is Work?
Unlike say - a homework set – for physical tasks work has a precise definition
  Linear Motion
    The product of distance moved times the opposing force
      Work = Force x Distance (pound – feet, Newton-meters)
      Lifting Task = Object Weight x Distance Moved
  Rotational Motion
    The product of angle rotated times the opposing torque
      Work = Torque x Angle (pound – feet, Newton-meters)
Notes: Abi

## Slide 7: What is Power?
Power is required to Work Quickly
Precise definitions for Physical Tasks
  Linear Motion
    The product of velocity moved times the opposing force
      Power = Force x Velocity (pound – feet/s, Newton-meter/s)
      Lifting Task = Object Weight x Velocity
  Rotational Motion
    The product of angular rate times the opposing torque
      Power = Torque x Angular Speed (pound-feet/s, Newton-meter/s or pound – feet x rpm, Newton-meter x rpm)
Notes: Abi

## Slide 8: Power
Power is conserved in a linked or closed loop system but not always in useful form.
  Ratio of Output Power / Input Power is called efficiency – varies from 0 to 1
  Heat loss is a double whammy
For Electrical Motors Mechanical Power is:
  Torque x Angular Speed = τω

## Slide 9: DC Motor Characteristics
Linear Relation between Torque and Angular Speed
Angular Speed (rpm)
Torque (oz-in)
0
Maximum
Speed
Maximum
Torque
Notes: Mikey

## Slide 10: Power
Power is Torque x Angular Speed
Angular Speed (rpm)
Torque (oz-in)
0
Max Power
Maximum
Speed
Maximum
Torque
Power (Watts)
Notes: Elizabeth

## Slide 11: Current Draw (Amperage)
Current draw is proportional to torque
Angular Speed (rpm)
Torque (oz-in)
0
Max Power
Maximum
Speed
Maximum
Torque
Current (Amps)
Power (Watts)
Maximum
Current
Notes: Elizabeth

## Slide 12: Motor Limitations
In many cases motors are current limited with respect to maximum achievable power
  See Example Next
Max torque / Max current is bad for motors!
  Circuit breakers aren’t fast enough to prevent motor destruction – they are designed to keep wiring from burning!!
    “Magic Blue Smoke” results
  Always protect against this!
    Time limit a motor that runs into a mechanical stop
    Place a detector to stop / reverse the motor before a mechanical stop

## Slide 13: Practical Example
40 Amp
Breaker
Banebots
40 Amp
Circuit
Breaker
Notes: Elizabeth

## Slide 14: Using Motors
Electrical Motors are intrinsically high speed / low torque devices – not highly useful out of the box
  Pulleys and Belts, Gears, Sprockets and Chain required to increase torque / lower speed for real utility
Notes: Connor

## Slide 15: Pulley Example
r1
v
1st Pulley
Attached to Motor
2nd Pulley
Attached to Device
Notes: Connor

## Slide 16
v
1st Pulley
Attached to Motor
Output Pulley
Attached to Device
Pulley Example

## Slide 17: Gear Example
Gear 1
Gear 2
Reversal of Direction
Notes: Connor

## Slide 18: Gears In Series

## Slide 19: Gears In Series
Appears highly difficult but generalizing the original gear example for any two gears “n” and “n+1” we have
Applied recursively starting with gears 1 and 2 we have

## Slide 20: Gears In Series
Don’t Effect Gear Ratio Calculations

## Slide 21: Gears in Parallel – Compound Gears
Individual Gear
Ratios Multiply
In Compound Gears
5:1
5:1
Overall Ratio is 5:1 x 5:1 = 25:1

## Slide 22: Planetary Gears
Planet Gears are Idler Gears
In a Planetary Gearbox

## Slide 23: Planetary Gear Stages
Motor
Input
Output Shaft
N:1
N:1
N:1
3-Stage Gearbox
Each Stage N:1
Total N3:1
Ring Gear
Very Compact!!!

## Slide 24: Motors – Power is Key!
The most important thing to look for in a motor is its overall Power capability!
  Then look at torque and speed individually
Use of gears, chains, belts will allow you to obtain the desired speed / torque combination for your application.

## Slide 25: 2017 Motors Ranked by Power
Brand | Type | Order # | Max Power (Watts) | Stall Torque (oz-in) | Free Speed (rpm)
RS775 | Pro | 217-4347 | 347.83 | 100.54 | 18700
Many | CIM | Varies | 337.34 | 343.40 | 5310
BaneBots | RS-775 | M7-RS775-18 | 266.79 | 110.93 | 13000
BaneBots | RS-550 | M5-RS550-12 | 245.83 | 68.85 | 19300
VEX | mini-CIM | 217-3371 | 227.40 | 198.26 | 6200
AndyMark | 9015 | am-0912 | 179.49 | 60.64 | 16000
VEX | BAG | 217-3351 | 146.71 | 56.64 | 14000
AndyMark | RS775-125 | am-2194 | 36.91 | 35.00 | 5700
AndyMark | RS775-5 | am-2161 | 36.91 | 35.00 | 5700
AndyMark | Snow Blower | am-2235 | 29.60 | 1600.00 | 100
Denso | Window | 5-163800-RC1 | 21.81 | 1309.91 | 90
Denso | Throttle | AE235100-0160 | 18.04 | 18.40 | 5300
AndyMark | NeveRest | am-3104 | 14.00 | 8.75 | 6600
Bosch | Seat Motor | 6004 RAE 194-06 | 13.83 | 3115.46 | 24

## Slide 26: 2017 Motors Ranked by Type
Brand | Type | Order # | Max Power (Watts) | Stall Torque (oz-in) | Free Speed (rpm)
RS775 | Pro | 217-4347 | 347.83 | 100.54 | 18700
Many | CIM | Varies | 337.34 | 343.40 | 5310
BaneBots | RS-775 | M7-RS775-18 | 266.79 | 110.93 | 13000
BaneBots | RS-550 | M5-RS550-12 | 245.83 | 68.85 | 19300
VEX | mini-CIM | 217-3371 | 227.40 | 198.26 | 6200
AndyMark | 9015 | am-0912 | 179.49 | 60.64 | 16000
VEX | BAG | 217-3351 | 146.71 | 56.64 | 14000
AndyMark | RS775-125 | am-2194 | 36.91 | 35.00 | 5700
AndyMark | RS775-5 | am-2161 | 36.91 | 35.00 | 5700
AndyMark | Snow Blower | am-2235 | 29.60 | 1600.00 | 100
Denso | Window | 5-163800-RC1 | 21.81 | 1309.91 | 90
Denso | Throttle | AE235100-0160 | 18.04 | 18.40 | 5300
AndyMark | NeveRest | am-3104 | 14.00 | 8.75 | 6600
Bosch | Seat Motor | 6004 RAE 194-06 | 13.83 | 3115.46 | 24

## Slide 27: Drive Motors
CIM Motors
  Heavy duty sealed bearing motor
    Can take continuous use and varying acceleration
  Also physically heavy
    Best mounted low in your robot for stability
  Use at least 4 in your Drive System
    Otherwise you will be pushed around by other robots
    Use 5th or 6th CIM for high power tasks
      2015 “Recycle Rush” – Tote / Garbage Can Lifter
      2016 “Stronghold” – Climbing Motor
      2017 “Steamworks” – Climbing Motor

## Slide 28: High Power Motors
Banebots 775-18
273 Watts
Banebots 550
254 Watts
Mini-CIM
229 Watts
Andy Mark 0912
179 Watts
Bag Motor
149 Watts
Use for high torque or high speed manipulators!!
VexPro 775 Pro
347 Watts

## Slide 29: Low Power Motors Highly Useful
RS-775-125 – am-2194
RS-775-5 – am-2161
Numerous Gearboxes,
Encoder And Mounting Kit
From AndyMark
For low power use (such as
Precision pointing)
NeveRest Motor
AndyMark’s principal
FTC motor
Very low power,
precision movement
Numerous Gearboxes,
Encoders And Mounting Kits
From AndyMark

## Slide 30: Low Power Dubious Utility
Denso
Throttle Motor
AE235100-0160
Denso
Window Motor
262100-3030 (Right)
262100-3040 (Left)
AndyMark
Snow Blower Motor
am-2235
Bosch Seat
Recliner Motor
82794153-3
Motors already attached to gears so reduction ratio is fixed. Difficult to mount. Difficult to wire. Awkward shapes.

## Slide 31: Gearboxes, Gears
CIM
  Andymark - www.andymark.com
  VexPro - www.vexrobotics.com/vexpro/
  Banebots - www.banebots.com
Other High Power
  Andymark, VexPro, Banebots
Low Power Highly Useful
  AndyMark
Low Power Dubious Utility
  Gearboxes built in – not needed
AM Mini
Toughbox
VexPro
VersaPlanetary
VexPro
Shifting
Gearbox
BaneBots
16:1
AM-3106
NeveRest 40
AM
PG-27

## Slide 32: Other Means of Reduction
Sprocket / Chain, Pulley / Belt, External Gears
  Typically used in single stage in combination with gearbox as manufactured to get the required speed torque
  Pulley Belt system requires precise or adjustable wheel positioning
  Gear Systems are heavy but least susceptible to slippage

## Slide 33: Drive Train Example
A single CIM is attached to a AndyMark Mini-Tough Box with 8.54:1 Reduction, the ½” output shaft is attached to a 1.45” diameter sprocket which is attached to a 2.683” sprocket on a 6” wheel. What is the maximum possible speed of the robot?

## Slide 34: Speed Calculations
Maximum CIM Speed is Free Speed 5310 rpm or 88.5 rev/s
Total Reduction
  8.54 x 2.863”/1.45” = 16.86
Rotational Speed at Wheel
  88.5 rev/s / 16.86 = 5.25 rev /s
Make | Part Number | Max Power (W) | Stall Torque (oz-in) | Free Speed (rpm)
CIM | FR801-001 | 337 | 343 | 5310

## Slide 35: Speed Calculations
Speed on 6” Wheel
  5.25 rev/s x Circumference = 5.25 rev/s x π x 6” = 99 “/ s = 8.2 ft/s

## Slide 36: Lift Calculations
A Banebots 775-18 Motor is attached to a 64:1 Gearbox to 1” radius sprocket which is drives a chain to lift an object. How heavy can the object be? How fast could the maximum weight object be lifted?

## Slide 37
40 Amp Circuit Breaker
49.1 oz-in torque

## Slide 38: Force Calculations
Banebots 775-18 has 49.1 oz-in torque with 40 amp circuit breaker
Using 64:1 gearbox torque increases to 49.1 oz-in x 64 = 3142.4 oz-in = 196.4 pound-in
Torque = Force x Distance
  Force = Torque / Distance = 196.4 pound-in / 1” = 196.4 pounds max

## Slide 39: Velocity Calculations
Motor Speed: 7422 rev/m at 40 amps = 123.7 rev/s
Gearbox shaft speed 123.7 / 64 = 1.93 rev/s
Velocity = 1.93 rev / s x Circumference = 1.93 rev/s x 2 x π x 1” = 12.14 in / s = 1.01 ft/s maximum

## Slide 40: Warning!!
Theoretical maximum performance will not be achieved in practice due to various energy losses.
  Always include a “performance margin” in your calculations!
  Test your system to insure it meets your requirements!

## Slide 41: Questions?
Contact Me
  Tom Milnes
  443-778-4982
  thomas.milnes@jhuapl.edu