## Slide 1: In the land of the blind, the one eyed man is king
Advanced Sensors for FRC Robots

## Slide 2: Agenda – Advanced Sensors for FRC Robots
Intermediaries
Inertial Sensors
LIDARs of various types
Vision
Fusion / Algorithms

## Slide 3: Intermediaries
Goal: Surround your Robot in Sensors!
Problem: The Robo-Rio only has limited inputs & CPU cycles
Solution: Breakout the task to a subordinate device!
  Microcontrollers
  Co-processors
  Other Robot Control Devices

## Slide 4: Microcontrollers
Small, cheap, relatively easy to use
Arduino, Teensy, Pic, ESP32, Feather, A-Star, MicroPython, Micro:Bit, ...
Do a great job if you are using them for “basic” sensor processing
Usually communicate via I2C or SPI

## Slide 5: Co-Processors
Usually full featured computers in their own right
Raspberry Pi, oDroid, Banana Pi, Pine, BeagleBone, Nvidia, …
Do a good job for computationally difficult sensors (e.g., Vision, SLAM)
Usually communicate via Ethernet

## Slide 6: Robot Control Devices
Certain sensors can plug directly into smart motor controllers!
The TalonSRX and SD540C both support Direct Limit Switch Inputs
The TalonSRX also supports more sensors (e.g., encoders, IMUs, potentiometers)

## Slide 7: And finally, the esoteric stuff…
Port Expanders: Can be easy to use for simple use cases (e.g., switches only)
FPGAs: Reprogrammable hardware devices (only use if you are a wizard)
You are much more likely to be on your own if you use these…

## Slide 8: Inertial Sensors
Inertial sensors mimic your inner ear – they can tell you how a robot is moving and oriented
Broken down into three common types:
  Accelerometers
  Gyroscopes
  Compasses

## Slide 9: Accelerometers
Accelerometers measure linear acceleration (in one axis)
So how do you get velocity or position?
  Hints: Multiple axes and Calculus!!!
Note! The low cost accelerometers we have on our robots have limited precision and lots of noise – integrating a noisy source can lead to errors in velocity and position

## Slide 10: Gyros
Gyroscopes (gyros) measure rotational velocity around a single axis
So how do you get Orientation?
  See previous hints!
Also, see previous notes re: low cost…

## Slide 11: Compasses
So, if we already can get orientation and velocity / position, what else do we need?
How about our orientation relative to the world!
  Accelerometers and gyroscopes provide a ‘local’ measurement, but cannot tell us how we are oriented to the field
Compasses measure our angle relative to the magnetic poles
  Q: So why do common packages have three compasses built in?

## Slide 12: Mixing Accelerometers, Gyros and Compasses
A common combination is a set of three accelerometer axes, three gyroscope axes and three magnetic compass axes into a package called an inertial measurement unit
The sensors can then work together to give various measurements we care about!

## Slide 13: Lidar / LIDAR / LiDAR / LADAR
Like Ultrasonics, LIDARs measure distance
  Come in various capabilities – 1 dimensional (like ultrasonics, just provide a distance in a single dimension), 2 dimensional (usually rotate around an axis), and 3 dimensional (provide an X/Y grid of distances)

## Slide 14: LIDARS (continued)
As you start going beyond ‘1D’ LIDARs, you are more likely to need a co-processor or similar to start processing (and making sense of) the distance data
However, 1D LIDARs can be quite useful – especially if you need a fairly narrow field of view

## Slide 15: Vision for FRC
Its possible to add a USB camera to the RoboRio and get a camera feed from your robot fairly easily
  Make sure to limit your framerate and resolution to what the field will support! (try 320x240@15-30fps)

## Slide 16: Processing Vision
FRC provides the GRIP set of tools to process images
  e.g., Lifecam HD3000 + Raspberry Pi + Networktables + OpenCV processing chain as produced by GRIP
Some teams are successfully using the Limelight camera, which hides a lot of vision complexity from the user

## Slide 17: Vision for advanced teams…
Neural Nets for game object recognition, stereo vision for depth perception, Robot Operating System, all can be integrated into FRC robots…
But make sure the game requires the effort to do so – these can be technically challenging…

## Slide 18: Fusion
Often sensors get more powerful when they can be combined with other sensors!
This is known as sensor fusion
Sensor fusion is particularly important for sensors that have processing delays

## Slide 19: Avoiding Lag
Example: How do you steer a robot to a goal?
Solution A:
  The robot stops
  The camera takes an image, and the co-processor figures out where the goal is
  The robot makes a motion plan to get there
  The robot acts on the next few seconds of that plan

## Slide 20: Accounting for Lag
Example: How do you steer a robot to a goal?
Solution B:
  The camera takes a picture, and the co-processor figures out where the goal is – the image is timestamped
  The robot uses the IMU to figure out where it was when the camera captured the image, and where it is now
  The robot continues to move to the updated plan